## Slide 1: BEGINNER PROGRAMMING LESSON
Introduction to the NXT Brick and Software

## Slide 2: Lesson Objectives
Learn how the NXT brick operates
Learn about the main components of the EV3 software

## Slide 3: The “Brick” Buttons
1 = Left, Right  Navigate menus
2 = Center Button  Select options Run Program Turn robot on
3 = Back  Undo Stop Program Turn robot off
1
1
3
2

## Slide 4: The “Brick” Screen
Menus on Screen
My Files Find programs you downloaded
2. Use left/right
buttons to find other menus such as “View”

## Slide 5: Ports, Sensors, motors
Ports 1, 2, 3, 4 = Sensors
Ports A, B, C = Motors
Default setup assumes Right Motor is in C, Left Motor is in B
B
C
Default setup
Front
Motors: make your robot move
Touch Sensor: Make your robot detect objects
Color sensor: Make your robot detect colors
Ultrasonic sensor: Make your robot measure distances

## Slide 6: EV3 Software
Open New Project
Open Saved Project

## Slide 7: EV3 Software: Starting A new program
Opened Projects
Opened Programs
Create a Project
Create a Program
Project Properties
List of programs

## Slide 8: PROJECTS VS. PROGRAMS
You will start by creating a PROJECT which has a .ev3 extension. You change the name of a project by using the Save Project As option from the File menu.
You will write many PROGRAMS as part of each PROJECT file. You change the name of a program within a project by doubling clicking on the program’s tab and typing in a new name.
Note: If there is an * next to the project name, you have made changes to the project and you have not yet saved yet.
There is a “x” next to project and program names. Clicking on it simply closes the file (it does not get deleted).
Here are some common file extensions in the EV3:
  Programs (.ev3p)
  Images (.rgf)
  Sounds (.rsf)
  Text (.rtf)
  Projects (.ev3) – the only type of file you can open with the EV3 software
  Import file (.ev3s) – can be imported by an EV3 project

## Slide 9: NAMING & SAVING YOUR WORK
Saving your Project
Select File and “Save Project As”
Changing the Program Name
Double click on ”Program”

## Slide 10: EV3 Software: Programming screen
Programming Blocks in
6 Colored Tabs
Programming Area or Canvas
Brick Status & Downloading

## Slide 11: Adding Blocks To Your Program
STEP 1: Green Block Tab, Click and hold any block and drag to programming area
STEP 2: Drop next to the Start Block (green arrow)
(See animation)

## Slide 12: Useful Icons
List Programs in Project: List of all programs in the project
Select: The cursor looks like an arrow and you can pick specific blocks or areas of the screen
Pan: The cursor looks like a hand. When you click and move the mouse, you can move through the program when it goes beyond one screen.
Comments: Click on this icon to create the comment box
Save Project: Save the current version of your project
Undo and Redo: Undo or redo the last actions
Zoom Out, Zoom In, and Reset Zoom: Use to decrease, increase or reset the magnification
1
2
3
4
5
6
7

## Slide 13: EV3 Blocks: Colored Tabs
ACTION BLOCKS
Move, Large & Medium Motor, Display…
FLOW BLOCKS
Start, Wait, Loop, Switch, Loop Interrupt
SENSOR BLOCKS
Brick Buttons, Gyro, Color, Ultrasonic
DATA OPERATIONS
Variables, Array, Logic, Math, Compare…
ADVANCED BLOCKS
Data Logging, Unregulated Motor…
MY BLOCKS
Custom Blocks you create
1
2
3
4
5
6
1
2
3
4
5
6

## Slide 14: CREDITS
Author: Sanjay and Arvind Seshan
More lessons are available at www.ev3lessons.com
This work is licensed under a Creative Commons Attribution-NonCommercial-ShareAlike 4.0 International License.