## Slide 1: BEGINNER EV3 PROGRAMMING Lesson 1
By: Droids Robotics
www.ev3lessons.com
Intro to Brick and Software, Moving Straight, Turning

## Slide 2: Section 1: EV3 BASICS

## Slide 3: The “Brick” Buttons
1 = Back Undo Stop Program Shut Down EV3
2 = Center Button Select options Run Program
3 = L, R, Up, Down Navigate menus
1
2
3
3
3
3

## Slide 4: The “Brick” Screen
Tabs on Screen
Run Recent Find programs you ran recently
2. File Navigation Find all programs by project
3. Brick Apps Port views
4. Settings Bluetooth, Wifi, Volume
1
2
3
4

## Slide 5: Ports, Sensors, motors
Ports 1, 2, 3, 4 = Sensors
Ports A, B, C, D = Motors
Default setup assumes Right Motor in C, Left Motor in B
B
C
Default setup

## Slide 6: EV3 Software
Open New Project
Open Saved Project

## Slide 7: EV3 Software: Starting A new program
Opened Projects
Opened Programs
Create a Project
Create a Program
Project Properties
List of programs

## Slide 8: EV3 Software: Programming screen
Programming Blocks in
6 Colored Tabs
Programming Area or Canvas
Brick Status & Downloading

## Slide 9: EV3 Blocks: Colored Tabs
ACTION BLOCKS
Move, Large & Medium Motor, Display…
FLOW BLOCKS
Start, Wait, Loop, Switch, Loop Interrupt
SENSOR BLOCKS
Brick Buttons, Gyro, Color, Ultrasonic
DATA OPERATIONS
Variables, Array, Logic, Math, Compare…
ADVANCED BLOCKS
Data Logging, Unregulated Motor…
MY BLOCKS
Custom Blocks you create

## Slide 10: Section 2: MOVING STRAIGHT

## Slide 11: CHALLENGE: Move Straight
STEP 1: Green Block Tab, Click and hold Move Steering and drag to programming area
STEP 2: Drop next to the Start Block (green arrow)

## Slide 12: Move STEERING Block
Steering: Straight or turn
Power/Speed
Duration/Distance
Mode of operation
Brake/Coast
B
C

## Slide 13: NEGATIVE & POSITIVE POWER: BACKWARD & FORWARD
Negative Power = Backwards
Positive Power = Forward

## Slide 14: CHALLENGE: Move Straight (3 SECONDS)
STEP 1: Green Block Tab, Click and hold Move Steering and drag to programming area
STEP 2: Drop next to the Start Block (green arrow)
STEP 3: Select Options. Move “3 Seconds”
STEP 4: Connect USB cable to EV3 and Laptop.
STEP 5: Download to EV3

## Slide 15: Move Straight: Seconds vs. degrees vs. rotations
CHALLENGE: Move your robot forward from the start line to the finish line (1) and back to the start (2).
Try: Select SECONDS, DEGREES or ROTATIONS
Try: Different speeds
What are some advantages or disadvantages of using each one?
Did you have to do a lot of guess and check to reach the line?
1
2
FINISH
START
B
C

## Slide 16: MOVE STRAIGHT CHALLENGE – PART 1 SUMMARY
TEAMS | SECONDS | DEGREES | ROTATIONS
Team 1 |  |  | 
Team 2 |  |  | 
Team 3 |  |  | 
Team 4 |  |  | 

## Slide 17: MOVE STRAIGHT discussion
Teams | Did you guess and check a lot? | Did changing the speed matter? | What was more accurate? Seconds? Degrees? | Do you think wheel size will matter? | Do you think battery level matters?
Team 1 |  |  |  |  | 
Team 2 |  |  |  |  | 
Team 3 |  |  |  |  | 
Team 4 |  |  |  |  | 

## Slide 18: Moving Straight more accurately: Use Port View
Try “port view” on brick (on Brick Apps tab)
  Move your robot with your hand from your start line to your end line
  Read how many degrees your robot moved
  Use this number in the Move Steering Block to move the correct distance.

## Slide 19: SECTION 3: TURNING

## Slide 20: PIVOT Vs. SPIN Turns
180 Degree Pivot Turn
180 Degree Spin Turn
Notice where the robot ends in both pictures after a 180 degree turn.
In the Spin Turn, the robot moves a lot less and that makes Spin Turns are great for tight positions. Spin turns tend to be a bit faster but also a little less accurate.
So when you need to make turns on the FLL board, you should decide which turn is best for you!
B
C
Start Position
End Position
Motors
B and C Move
B
C
Motor
B Moves
Start Position
End Position
B
C
B
C

## Slide 21: How to Make Pivot and Spin turns
Steering Value |  |  | 
50 | -50 | 100 | -100
Pivot Turn Right | Pivot Turn Left | Spin Turn Right | Spin Turn Left
Change Steering value here
B
C
B
C
B
C
B
C

## Slide 22: MAKING A Pivot turn for 90 DEGREES
Program your robot to turn 90 degrees....Does the robot actually turn 90 degrees if you just pick 90 degrees for distance?
B
C
B
C
?

## Slide 23: how do you make the robot turn 90 degrees?
Ans. Try using the port view again to measure the turn and then input the correct number of degrees.

## Slide 24: TURNING An Attachment ARM, not just the wheels
Attach a medium motor to Port A or a large motor to Port D as needed.
Move Steering vs. Motor Block
  For moving your wheels you should use a Move Steering Block that syncs both wheel motors.
  For moving your attachment your arm, you use either a Medium Motor Block or a Large Motor Block because you don’t need to sync your motors.
Medium Motor Block
Large Motor Block

## Slide 25: Motor “On” and “Wait” Blocks
Leaving the motor “on” and “off”
Why use the “on” instead of “degrees”?
  May want the program to do other tasks while moving
“Wait” block in Flow Tab
  Wait for seconds
WAIT!

## Slide 26: Something fun: Display Block
Use the Display Block to display information and pictures on the screen
You can control the location and size of text
You can use this same block to display sensor readings and instructions.
Challenge: Can you display eyes on the screen while moving? Alternate eyeballs that look left and right.
  Use the Display Block, Motor On and Wait Block

## Slide 27: CHALLENGE Solution
Display Block
Motor On
Wait Block
Motor Off

## Slide 28: CREDITS
This tutorial was created by Sanjay Seshan and Arvind Seshan from FLL Team Not the Droids You Are Looking For (Droids Robotics)
We have additional material for more advanced lessons available on request.
Useful tools for FLL teams and robot programmers are available at www.ev3lessons.com
The material is made available to you free of charge. However, we would greatly appreciate a letter indicating that you are using the materials and what you think of them.
Feedback and suggestions are encouraged.
Email: team@droidsrobotics.org